## Slide 1: Storage - Disks
Slides include materials from Operating System Concepts, 7th ed., by Silbershatz, Galvin, & Gagne, Distributed Systems: Principles & Paradigms, 2nd ed. By Tanenbaum and Van Steen, and Modern Operating Systems, 2nd ed., by Tanenbaum

## Slide 2: Storage
Where is your stuff when you turn your machine off?
  In “the cloud”!
Where does the cloud store your stuff?
Various storage devices
  Magnetic tape
  “Hard disk”
  CD-ROM
  Flash memory
What do they have in common? How do they differ?

## Slide 3: Storage characteristics
“Non-volatile”
  Write; power-off; read: should return same value
    Years later!
Slow (compared to RAM)
  Milliseconds or seconds instead of nanoseconds Can't execute programs from it (must fetch first)
“Block oriented”
  Fetch and store large clumps of data
    Spinning disk: 512/4096 bytes
    CD-ROM: 2048 bytes
    Flash: “hard to say”
  Time to fetch 1 byte == time to fetch 1 block

## Slide 4: Storage Model
Address space
  Blocks have numbers
  Ancient times: (C,H,S) tuple
    C, H, S were geometric features of old disks
  Modern: (LBA)
    “Logical Block Address” runs from 0..N

## Slide 5: Storage Model
Reading and writing
  Read-block(N) ⇒ [huge delay] ⇒ block else failure
    Sometimes a re-try helps (usually not)
  Write-block(N) ⇒ [huge delay] ⇒ “ok” else failure
    Failures usually indicate “obvious” bad things
      The disk motor stopped
    “Successful” write doesn't guarantee a later read
    Devices usually contain a power buffer
      A write operation either completes or has no effect
  Modern devices support “tagged command queueing”
    OS can issue multiple requests, each has a “tag”
    Device can return results in any order, with the OS's tag

## Slide 6: Command Queueing In Act
Disks serve read requests out of order
  OS queues: “read 37”, “read 83”, “read 2”
    Disk returns 37, 2, 83
      Great! That's why we buy smart disks and queue multiple requests
Disks serve write requests out of order, too
  OS queues “write 23”, “write 24”, “write 1000”, “read 4-8”, ...
    Disk writes 24, 23 (!!), gives you 4, 5, 6, 7, 8, writes 1000
    What if power fails before last write?
    What if power fails between first two writes?

## Slide 7: Command Queueing In Action
How can OS ensure data-structure integrity?
  Special commands
    “Flush all pending writes”
      Think “my disk is 'modern'”, think “disk barrier”
      Can even queue a flush to apply to all before now
      Can apply these “barrier” flushes to subsets of requests
      Rarely used by operating system
    “Disable write cache”
      Think “please don't be quite so modern”

## Slide 8: Examples
“Hard drive”
  Parts
  Execution model
NAND flash memory
  Challenges
    Write amplification
    Wear leveling

## Slide 9: Anatomy of a Hard Drive
Information is written to and read from the platters by the read/write heads on the end of the disk arm
https://www.youtube.com/watch?v=NtPc0jI21i0

## Slide 10: Anatomy of a Hard Drive
The arm is moved by a voice coil actuator
Slow, as computers go
  Acceleration time
  Travel time

## Slide 11: Anatomy of a Hard Drive
Both sides of each platter store information
Each side of a platter is called a surface
Each surface has its own read/write head

## Slide 12: Anatomy of a Hard Drive
Each surface is divided by concentric circles, creating tracks
These tracks are further divided into sectors
A sector is the smallest unit of data transfer to or from the disk
  512 bytes – traditional disks
  2048 bytes – CD-ROMs
  4096 bytes – 2010 disks
    (pretend to be 512!)
“Sector address”
  “C/H/S”

## Slide 13: Anatomy of a Hard Drive, Actual
Modern hard drives use zoned bit recording
  Disk has tables to map track# to #sectors
  Sectors are all roughly the same linear length
  LBA “sector address” names a sector, like “page number” names a frame

## Slide 14: Anatomy of a Hard Drive
We need to do two things to transfer a sector
  Move the read/write head to the appropriate track (“seek time”)
  Wait until the desired sector spins around (“rotational delay”/“rotational latency”)
Observe
  Average seeks are 2 – 10 msec
  Rotation of 5400/7200/10K/15K rpm means rotational delay of 11/8/6/4 msec
  Rotation dominates short seeks, matches average seeks

## Slide 15: Anatomy of a Hard Drive
Observe
  Average seeks are 2 – 10 msec
  Rotation of 5400/7200/10K/15K rpm means rotational delay of 11/8/6/4 msec
  Rotation dominates short seeks, matches average seeks

## Slide 16: Anatomy of a “Sector”
Finding a sector involves real work Locate correct track; scan sector headers for number
After sector is read, compare data to checksum

## Slide 17: Disk Cylinder
Matching tracks across surfaces are collectively called a cylinder

## Slide 18: Access Within A Cylinder is Faster
Heads share one single arm
  All heads always on same cylinder
  Active head is aligned, others are “close”
Switching heads is “cheap”
  Deactivate head I, activate J
  Read a few sector headers to fine-tune arm position for J's track
Optimal transfer rate?
  Transfer all sectors on a track
  Transfer all tracks on a cylinder
  Then move the arm

## Slide 19: Access Time
On average, we will have to move the read/write head over one third of the tracks
  The time to do this is the “average seek time”
    5400 rpm: ~10 ms
    7200 rpm: ~8.5 ms
We will also must wait half a rotation, on average
  The time to do this is “average rotational delay”
    5400 rpm: ~5.5 ms
    7200 rpm: ~4 ms
These numbers don't exactly add
  While arm moves sideways, disk spins below it

## Slide 20: Access Time
Total random access time is ~7 to 20 milliseconds
  1000 ms/second, 20 ms/access = 50 accesses/second
  50 1⁄2-kilobyte transfers per second = 25 KByte/sec
Disks are slow!
  But Disk transfer rates are hundreds of MBytes/sec!
What can we, as OS programmers, do about this?
  Read/write more per seek (multi-sector transfers)
    Disk cache can read ahead and delay/coalesce writes
  Don't seek so randomly
    Place data near also-relevant data
    Re-order requests
      OS may do “disk scheduling” instead of a FIFO queue
      (Disks internally schedule too)

## Slide 21: Solid-State Disks (SSD)
What is “solid state”?
  Original meaning: “no vacuum tubes”
  Modern meaning: “no moving parts”
What is “solid state” storage?
  RAM backed by a battery!
  “NOR flash”
  “NAND flash”
  Newer things

## Slide 22: Solid-State Disks (SSD)
What is “solid state” storage?
  RAM backed by a battery!
    Fast
“NOR flash”
  Word-accessible
  Writes are slow, density is low
  Used to boot embedded devices, store configuration
“NAND flash”
  Read/write “pages” (512 B), erase “blocks” (16 KB)
  Most SSDs today are NAND flash

## Slide 23: Solid-State Disks (SSD)
Architectural features of NAND flash
  No moving parts means no “seek time” / “rotational delay”
  Read is faster than write
  Write and “erase” are different
    A blank page can be written to (once)
    A written page must be erased before rewriting
    But pages can't be individually erased!
      “Erase” works on multi-page blocks (16 KB)
      “Erase” is very slow
      “Erase” damages the block each time
Implications
  “Write amplification”
  “Wear leveling”

## Slide 24: SSD Concepts
SSD
……………………………………………………………………………………………………………………………………………………………………………………………………………
PAGE
BLOCK

## Slide 25: SSD: Updating data via read/erase/write
Goal: update 8 pages (4 KB) in a block (16 KB)
Update
these
pages
SSD

## Slide 26: SSD: Updating data via read/erase/write
Goal: update 8 pages (4 KB) in a block (16 KB)
Fast
READ
RAM Memory
SSD

## Slide 27: SSD: Updating data via read/erase/write
Goal: update 8 pages (4 KB) in a block (16 KB)
Update
RAM Memory
SSD

## Slide 28: SSD: Updating data via read/erase/write
Goal: update 8 pages (4 KB) in a block (16 KB)
ERASE!
Slow
RAM Memory
SSD
Wears out

## Slide 29: SSD: Updating data via read/erase/write
Goal: update 8 pages (4 KB) in a block (16 KB)
WRITE
Slow
RAM Memory
SSD

## Slide 30: “Write Amplification”
Goal: update 8 pages (4 KB) in a block (16 KB)
Result
  Logical: wrote 4 KB
  Physical: erased and write 16 KB
  “Amplification factor”: 4
    Why do we care? Device will wear out 4X faster!
SSD

## Slide 31: Hot-Spot Wear and Wear Leveling
The bad case
  File systems like to write the same block repeatedly
  Erasing damages part of the flash
    ~10,000 erases destroys a block
Strategy: lie to the OS!
  Host believes it is writing to specific “disk blocks” - LBA
  Store the information somewhere else!
    Secretly re-map host address onto NAND address
    FTL - “flash translation layer”
Each part of the “disk” moves from one part of the flash to another over time
  “Over-provision”
    Advertise less space than there really is
    Use spare space to replace worn-out blocks
  Use up overprovisioning as blocks wear out
    Device eventually gets slower and then fails

## Slide 32: Managing - Write Amplification
The bad case
  Small random writes
Strategy: lie to the OS!
  Group multiple small writes into full blocks
    Write at sequential write rates
  To update a “disk block”, store a new copy somewhere else
    Leaves “holes” in other blocks (stale old block versions)
    At some point, “clean out” the holes by reading a bunch of old blocks and writing back a smaller number of whole pages
  Rate of cleaning depends amount of unallocated space
    Controller reserves X% hidden space (ie. 10, 20, 50%)

## Slide 33: SSD vs Disk
SSD's implement “regular disk” model
  LBA sectors
  Write-sector, read-sector, “park heads”, etc.
Read operations are extremely fast (100X faster), no “seek time” or “rotational delay” (every sector is “nearby”)
Write operations “vary widely” (maybe 100X faster, maybe not faster at all)
SSD's use less power than actual disks (~1/5?)
SSD's are shock-resistant
Writing to an SSD wears it out much faster than a disk
SSD's are expensive (20X or more)

## Slide 34: SSD Drives - Summary
Solid State disks have no moving parts and mechanical delays.
SSD’s have other problems due to the following characteristics:
  Block based read only read access, fast, no restriction.
  Only empty blocks can be written, slower than read but still fast
  Non-empty blocks needs to be erased.
  Erasing has to be done in larger units (segments/clusters). i.e. 512byte vs. 32KByte.
  Erasing is slow and each segment has a erase cycle limit (i.e. 10000 erases).
Single bit update requires:
  Erase a whole segment , write all (32K) content with modified bit.

## Slide 35: SSD Drives - Summary
Erase/write problem solution:
  Write modified blocks on already erased segments
  Logical block number and actual block on disk differs.
  Keep and internal table for actual block to logical block mapping.
  OS asks for logical block content, SDD controller returns actual block content.
Called Wear Leveling or Write Amplification.
FTL: Flash Translation Layer implemented on Flash hardware does the translation. OS does not know about it.
OS based solution: Use a Log Structured File System.
  To be discussed in detail in FileSystems

## Slide 36: Disk Management
Managing disks on a system gets complicated as space requirement increases by time.
Adding new disks to system, changing failed disks, deleting disks, adjusting partitions with new layout is an issue.
A solution is Logical Volume Management.
  A layer in OS maps a group of physical disk partitions into a large contiguous logical volume.
    E.g. add 5 4T disks to get a 20T as a single partition.
  LVM helps getting OS independent from underlying disk organization.
RAID (Redundant Array of Independent Disks) is another solution which also respects disk failures and efficiency.
Common RAID levels:
  0 stripe (distribute I/O requests on two or more disks for efficiency)
  1 mirror (execute same I/O on two or more disks for failure recovery)
  5 distributed parity (distribute operation on multiple disk with parity, both efficiency and filure recovery)
RAID is best implemented in HW. OS implementation is called Soft RAID

## Slide 37: Further reading
Reliably Erasing Data from Flash-based Solid State Drives
  Wei et al., UCSD FAST '11 http://www.usenix.org/legacy/events/fast11/tech/full_papers/Wei.pdf
A Conversation with Jim Gray
  Dave Patterson
  ACM Queue, June 2003 http://queue.acm.org/detail.cfm?id=864078
Terabyte Territory
  Brian Hayes
  American Scientist, May/June 2002 http://www.americanscientist.org/issues/pub/terabyte-territory